## Slide 1: Reliability Estimation in Series Systems
Maximum Likelihood Techniques for Right-Censored and Masked Failure Data Alex Towell

## Slide 2: Introduction
Notes: Testing

## Slide 3: Context & Motivation
  Quantifying reliability is crucial for system design and maintenance.
  We often only have system-level failure data.
  Masked and right-censored data obscure reliability estimates.
  Makes it difficult to estimate component reliability.
  Need robust techniques to decipher this data and make accurate estimations.

## Slide 4: Core Contributions
  Derivation of likelihood model that accounts for right-censoring and masking.
    Trivial to add more failure data via a likelihood contribution model.
    R Library: github.com/queelius/wei.series.md.c1.c2.c3
  Clarification of the assumptions required for the likelihood model.
  Simulation studies with Weibull distributed component lifetimes.
    Assess performance of MLE and BCa confidence intervals under various scenarios.

## Slide 5: Series System

## Slide 6
A lot of complex systems have critical components .
  One component fails, the system fails.
  “A chain is only as strong as its weakest link.” - Thomas Reid
  We call these series systems. Let be the lifetime of system .
    is the lifetime of component in system .

## Slide 7: Reliability Function: System Longevity
Definition: Represents the probability that a system or component functions beyond a specified time :
Interpretation:
  A high reliability value indicates a lower probability of failure.
  Essential for understanding the longevity and dependability of systems and components.
Series System Reliability: Product of the reliabilities of its components:
Relevance: Forms the basis for most reliability analyses and helps in making informed decisions about system design and maintenance.
  Directly used in our likelihood model for right-censoring events.

## Slide 8: Hazard Function: Failures Characteristics
Definition: Instantaneous failure rate at a specific time, given survival up to that point:
Interpretation
  A tool to understand how failure risk evolves over time.
  Guides maintenance schedules and interventions.
  Failure characteristics:
    Rising: wear-out (aging).
    Declining: infant mortality (defects).
    Constant: random (accidents).
Series System Hazard Function: Sum of the hazard functions of its components:

## Slide 9: Component Cause of Failure
Let denote component cause of failure of system.
  The probability that the component causes failure:
  The conditional probability that the component causes a failure, given that the system failed at time :
  Joint Distribution of System Lifetime and Component Cause of Failure
  Relevance: Important in our likelihood model for masked failures.

## Slide 10: Reliability of Well-Designed Series Systems
  MTTF is a summary measure of reliability:
    Equivalent to integrating its reliability function over its support.
    MTTF can be misleading. We can’t assume components with longer MTTFs are more reliable.
  A series system is only as strong as its weakest component.
  In a well-designed series system, components have similar failure characteristics:
    Similar MTTFs and probabilities of being the cause of failure.
  Relevance: Our simulation study is based on a (reasonably) well-designed series system.

## Slide 11: Likelihood Model

## Slide 12
We have our system model, but we don’t observe component lifetimes. We observe data related to component lifetimes.
Observed Data
  Right censoring: No failure observed.
    The experiment ended before the system failed.
      is the right-censoring time.
      indicates right-censoring for system .
  Masked causes
    The system failed, but we don’t know the component cause.
      is the observed time of system failure.
      indicates system failure for system .
      are a subset of components that could have caused failure.

## Slide 13: Observed Data Example
Observed data with a right-censoring time for a series system with components.

## Slide 14
System | Right-censored lifetime | Event indicator | Candidate set
1 |  |  | 

## Slide 15: Data Generating Process
DGP is underlying process that generates observed data:
  Green elements are observed.
  Red elements are unobserved (latent).
  Candidate sets () related to component lifetimes ( and other (unknown) covariates.
    Distribution of candidate sets complex. Seek a simple model valid under certain assumptions.

## Slide 16: Likelihood Function
Assumptions
  Right-censoring time independent of component lifetimes and parameters:
  Observed failure time with candidate sets. Candidate sets satisfy some conditions (discussed later).
Likelihood Contributions

## Slide 17: Likelihood Contribution: Masked Failures
Masking: When a system fails, but the precise failed component is ambiguous.
**To make problem more tractable, we introduce certain conditions
  Reasonable for many real-world systems.

## Slide 18: Masking Conditions
Candidate Set Contains Failed Component: The candidate set, , always includes the failed component:
Equal Probabilities Across Candidate Sets: For an observed system failure time and a candidate set , the probability of of the set is constant across different component failures within the set:
for every .
Masking Probabilities Independent of Parameters: The masking probabilities when conditioned on and failed component aren’t functions of .

## Slide 19: Likelihood Contribution: Masked Component Cause of Failure
Joint distribution of , , and :
Marginalize over and apply Conditions 1, 2, and 3:
Result: We don’t need to model the distribution of the candidate sets .
  .

## Slide 20: Methodology: Maximum Likelihood Estimation
Maximum Likelihood Estimation (MLE): Maximize the likelihood function:
Solution: Numerically solved system of equations for :

## Slide 21: Bootstrap Method: Confidence Intervals
Sampling Distribution of MLE: Asymptotic normality is useful for constructing confidence intervals.
  Issue: May need large samples before asymptotic normality holds.
Bootstrapped CIs: Resample data and find an MLE for each. Use the distribution of the bootstrapped MLEs to construct CIs.
  Percentile Method: Simple and intuitive.
Correctly Specified CIs: A coverage probability close to the nominal level of .
  Issue: Coverage probability may be too low or too high.
  Adjustments: To improve coverage probability, we use the BCa method to adjust for bias (bias correction) and skewness (acceleration) in the estimate. Coverage probabilities above acceptable.

## Slide 22: Challenges with MLE on Masked Data
We discovered some challenges with the MLE on masked data.
Convergence Issues: Flat likelihood regions were observed due to the ambiguity in the masked data and small sample sizes.
Bootstrap Issues: Bootstrap relies on the Law of Large Numbers.
  Bootstrap might not represent the true variability, leading to inaccuracies.
  Due to right censoring and masking, the effective sample size is reduced.
Mitigation: We discard non-convergent samples for the MLE on original data, but keep all resamples for the bootstrap.
  This ensures that the bootstrap for “good” data is representative of the variability in the original data.
  We report convergence rates in our simulation study.

## Slide 23: Series System with Weibull Component Lifetimes

## Slide 24
Weibull Distribution: We model a system’s components using Weibull distributed lifetimes.
The lifetime distribution for the component of the system is:
Where:
  is the scale parameter.
  is the shape parameter.
Significance of the Shape Parameter:
  : Indicates infant mortality. E.g., defective components weeded out early.
  : Indicates random failures. E.g., result of random shocks.
  : Indicates wear-out failures. E.g., components wearing out with age.

## Slide 25: Theoretical Results
Reliability and hazard functions of a series system with Weibull components: where is the parameter vector of the series system.
Likelihood Model
Right Censoring and Masked Failures: The likelihood contribution of system:

## Slide 26: Simulation Study Overview

## Slide 27
This study is centered around the following well-designed series system with Weibull component lifetimes:

## Slide 28
Component | Shape | Scale | MTTF | 
1 | 1.26 | 994.37 | 924.87 | 0.17
2 | 1.16 | 908.95 | 862.16 | 0.21
3 | 1.13 | 840.11 | 803.56 | 0.23
4 | 1.18 | 940.13 | 888.24 | 0.20
5 | 1.20 | 923.16 | 867.75 | 0.20
System | NA | NA | 222.88 | NA

## Slide 29: Performance Metrics
Objective: Evaluate the MLE and BCa confidence intervals’ performance across various scenarios.
  MLE Evaluation:
    Accuracy: Proximity of the MLE’s expected value to the actual value.
    Precision: Consistency of the MLE across samples.
  BCa Confidence Intervals Evaluation:
    Accuracy: Confidence intervals (CIs) should cover true parameters around of the time.
      Coverage probability (CP)
    Precision: Assessed by the width of the CIs.
Both accuracy and precision are crucial for confidence in the analysis.

## Slide 30: Data Generation
We generate data for systems with components each. We satisfy the assumptions of our likelihood model by generating data as follows:
  Right-Censoring Model: Right-censoring time set at a known value, parameterized by the quantile .
    Satisfies the assumption that the right-censoring time is independent of component lifetimes and parameters.
  Masking Model: Using a Bernoulli masking model for component cause of failure, parameterized by the probability .
    Satisfies masking Conditions 1, 2, and 3.

## Slide 31: Scenario: Impact of Right-Censoring
Vary the right-censoring quantile (): to . Fixed the parameters: and .
Background
  Right-Censoring: No failure observed.
  Impact: Reduces the effective sample size.
  MLE: Bias and precision affected by censoring.

## Slide 32: Scale Parameters
  Dispersion: Less censoring improves MLE precision.
  Bias: Both parameters are biased. Bias decreases with less censoring.
  Median-Aggregated CIs: Bootstrapped CIs become consistent with more data.

## Slide 33: Shape Parameters
  Dispersion: Less censoring improves MLE precision.
  Bias: Both parameters are biased. Bias decreases with less censoring.
  Median-Aggregated CIs: Bootstrapped CIs become consistent with more data.

## Slide 34: Coverage Probability and Convergence Rate
\begin{figure}
% \begin{minipage}{.5} \end{minipage} \end{figure}
  Calibration: CIs converge to . Scale parameters better calibrated.
  Convergence Rate: Increases as right-censoring reduces.

## Slide 35: Conclusion
  MLE precision improves, bias drops with decreased right-censoring.
  BCa CIs perform well, particularly for scale parameters.
  MLE of most reliable component more affected by right-censoring.

## Slide 36: Impact of Masking Probability
Vary the masking probability : to . Fixed the parameters: and .
Background
  Masking adds ambiguity in identifying the failed component.
  Impacts of masking on MLE:
    Ambiguity: Higher increases uncertainty in parameter adjustment.
    Bias: Similar to right-censoring, but affected by both and .
    Precision: Reduces as increases.

## Slide 37: Scale Parameters
  Dispersion: Increases with , indicating reduced precision.
  Bias: Positive bias rises with .
  Median-Aggregated CIs: Widen and show asymmetry as grows.

## Slide 38: Shape Parameters
  Dispersion: Increases with , indicating reduced precision.
  Bias: Positive bias rises with .
  Median-Aggregated CIs: Widen and show asymmetry as grows.

## Slide 39: Coverage Probability and Convergence Rate
\begin{figure}
% \begin{minipage}{.45} \end{minipage} \end{figure}
Calibration: Caution advised for severe masking with small samples.
  Scale parameters maintain coverage up to .
  Shape parameters drop below after .
Convergence Rate: Reduces after , consistent with CP behavior.

## Slide 40: Conclusion
  Masking influences MLE precision, coverage probability, and introduces bias.
  Despite significant masking, scale parameters have commendable CI coverage.

## Slide 41: Impact of Sample Size
Assess the impact of sample size on MLEs and BCa CIs.
  Vary sample size : to
  Parameters: ,
Background
  Sample Size: Number of systems observed.
  Impact: More data reduces uncertainty in parameter estimation.
  MLE: Mitigates biasing effects of right-censoring and masking.

## Slide 42: Both Scale and Shape Parameters

## Slide 43: Parameters
  Dispersion:
    Dispersion reduces with —indicating improved precision.
    Disparity observed between components and .
  Bias:
    High positive bias initially, but diminishes around .
    Enough sample data can counteract right-censoring and masking effects.
  Median-Aggregated CIs:
    CIs tighten as grows—showing more consistency.
    Upper bound more dispersed than lower, reflecting the MLE bias direction.

## Slide 44: Coverage Probability and Convergence Rate
\begin{figure}
% \begin{minipage}{.4} \end{minipage} \end{figure}
  Calibration:
    CIs are mostly above across sample sizes.
    Converge to as grows.
    Scale parameters have better coverage than shape.
  Convergence Rate:
    Improves with , surpassing for .
    Caution for estimates with in specific setups.

## Slide 45: Conclusion
  Sample size significantly mitigates challenges from right-censoring and masking.
  MLE precision and accuracy enhance notably with growing samples.
  BCa CIs become narrower and more reliable as sample size increases.

## Slide 46: Conclusion

## Slide 47: Part 1
Key Findings
  Employed maximum likelihood techniques for component reliability estimation in series systems with masked failure data.
  Methods performed robustly despite masking and right-censoring challenges.
Simulation Insights
  Right-censoring and masking introduce positive bias; more reliable components are most affected.
  Shape parameters harder to estimate than scale.
  Large samples can counteract these challenges.

## Slide 48: Part 2
Confidence Intervals
  Bootstrapped BCa CIs demonstrated commendable coverage probabilities, even in smaller sample sizes.
Takeaways
  Framework offers a rigorous method for latent component property estimation from limited observational data.
  Techniques validated to provide practical insights in diverse scenarios.
  Enhanced capability for learning from obscured system failure data.

## Slide 49: Discussion